## Slide 1
Path Representation and Intermediate Shapes
Shape representation
DLO is discretized into N = 21 nodes.
Each 2D shape is represented as X_j in R^(21 x 2).
Given initial shape X_0 and target shape X_g.
Planned path
X_0 -> X_1 -> ... -> X_M -> X_g
Full planned path: X_path in R^(K x 21 x 2)
Linear reference initialization
R_j = (1 - alpha_j) X_0 + alpha_j X_g
alpha_j = j / (K - 1)
Optimization role
The interpolation is only a reference.
Final path is obtained by optimizing intermediate shapes
under length and bending constraints.
Variable | Meaning | Dimension
X_j | 2D DLO shape at path index j | 21 x 2

## Slide 2
Intermediate-shape Optimization
Main objective
J_shape = w_ref J_ref + w_len J_len + w_bend J_bend + w_time J_time
J_ref = sum_j ||X_j - R_j||^2
J_len = sum_j sum_i (||p_(i+1)^j - p_i^j|| - Delta s)^2
J_bend = sum_j ||D_2 X_j||^2
J_time = sum_j ||X_(j+1) - X_j||^2
Quantity | Dimension / Definition
X_j | R^(21 x 2)
D_1 | R^(20 x 21)
D_2 | R^(19 x 21)
Delta s | L / (N - 1)
Implementation logic
1. Initialize X_path by linear interpolation.
2. Smooth intermediate shapes.
3. Penalize bending using D_2.
4. Resample each shape by arc length.
5. Keep X_0 and X_g fixed.
6. Output planned_shapes.shape = (K, 21, 2).

## Slide 3
Three-force Inverse Actuation
Transition target
For each transition: X_j -> X_(j+1)
delta q_j = vec(X_(j+1) - X_j) in R^42
u_j = [s_1, s_2, s_3, F_x1, F_y1, F_x2, F_y2, F_x3, F_y3]
Force spacing: |s_a - s_b| >= 0.01 m
Force mapping and stiffness
F_node = A(s) f
K delta q = A(s) f
K = EA(D_1^T D_1) kron I_2 + EI(D_2^T D_2) kron I_2 + epsilon I
Given force positions s: B(s) = K^-1 A(s)
f* = (B^T B + lambda I)^-1 B^T delta q_j
Quantity | Dimension
delta q_j | R^42
K | R^(42 x 42)
A(s) | R^(42 x 6)
f | R^6
Final outputs
planned_shapes.npy
force_actions.csv
length_error.csv
bending_energy.csv